| To: | Prof. Juerg M. Matter Project Director, Oman Drilling Project | Doc. No.: AZD/ODP/GT-2A/DPR-25 Dated: 18-01-2017 |
| --- | --- | --- |
| Client : | Oman DP | Consultant : AZD Engineering Consultancy |
| Contractor : | Lalbuksh Voltas | Sub-contractor: Geo-Solutions Engineering |
| Subject : Daily Progress Report |
| Project : Phase-1: OmanDP - Scientific Drilling Programme for Oman Drilling Project in Ash Sharqiyah North Governorate and Ad Dakhiliyah Governorate |

DAILY PROGRESS REPORT

(Dated: 18th of January 2017)

Rig-1 (Dynatech)

LOCATION AND TARGET:

Drill Hole ID : GT-2A Location : Wadi Gideah Coordinates : UTM: E655960.7 N2529193.5 Azimuth : 54 ºN; Inclination : 60º Drilling : HQ/NQ Size; Method : Wire line-Diamond Core Drilling Target Depth : 400 mtrs Geol. Target : Gabbro-Transition from Foliated to Layered

DRILLING:

Drilling Status : -Cleaned the hole at bottom. NQ drill assembly pulled out of hole. -Reamed the hole and extended HW surface casing up to 6.8m; further reaming not possible with the increased pressure. -HQ casing with shoe bit pulled out of hole and drill hole covered with safety. Today’s Drilling : - Cumulative Total : 400 m (HQ=149.7m; NQ=250.3 m)

CORE CURATION:

Core Scanning, Labeling, Sketching, Description, Sampling, and Storage etc. being performed as per the standard procedure. Core box replacement and proper cover fixing in progress.

OTHER ISSUES:

Contractual Issues : None Technical Issues : None Health & Safety Issues: None Logistic Issues : None

Remarks : Peter Kelemen, Juergen Koepke and Dieter Garbe leave the site. Visit to GT-1 Site for arrangement prior to shifting.

Regards,

Nehal H Warsi

Site Geologist, AZD Engineering Consultancy

GSM:  +968 98037217; 79113454

Email: nhwarsi@gmail.com