Supplementary data Text-U1373A-C-Sedimentology-S1

Petrographic characteristics and occurrences of volcaniclasts in Unit I and III

TYPE: 1

TEXTURE: moderately plagioclase-olivine-phyric basalt

COLOR: light reddish gray

PHENOCRYSTS: 1% olivine (altered) max: 2 mm, mod: 1.5 mm; 3% plagioclase (fresh) max: 1.5 mm, mod: 1 mm.

GROUNDMASS: fine grained

VESICLES: 3%, elongate, subangular, filled with zeolite and carbonate

ALTERATION: moderately to highly altered brownish gray basaltic clast, olivine is completely altered to iddingsite

VEINS:

OCCURRENCE: 1R 1A 3-5 cm, 1R 3A 19-27 cm, 3R 3A 21-26 cm, 41-45 cm, 54-60 cm; 5R 2A 55.5-59.5 cm, 60-71 cm, 71.5-80.5 cm, 81.5-94 cm

==========================================================

TYPE: 2

TEXTURE: aphyric basalt

COLOR: brownish gray

PHENOCRYSTS: none

GROUNDMASS: fine grained

VESICLES: 0-10%, elongate, subrounded, mainly filled with carbonate and minor zeolite

ALTERATION: moderately to highly altered brownish gray basaltic clast, presence of reddish halos (oxidizing conditions), minor olivine is completely altered to iddingsite

VEINS:

OCCURRENCE: 1R 1A 6-14 cm, 22-73 cm, 75-80 cm; 1R 2A 28-41 cm, 77-84 cm; 1R 3A 19-27 cm; 3R 2A 66-74 cm; 3R 3A 29-32 cm; 70-74 cm; 102-107 cm; 3R 4A 12-13 cm; 5R 1A 0-37 cm, 90-107 cm, 110-117 cm, 137-145 cm; 5R 2A 94-101 cm; 6R 2A 1-6 cm, 13-20 cm, 26-29 cm, 46-49 cm, 67-71 cm, 76-83 cm, 85-88 cm, 86-89 cm; 7R 1A 37-40 cm; 7R 1A 49-53 cm

==========================================================

TYPE: 3

TEXTURE: aphyric basalt

COLOR: light gray

PHENOCRYSTS: 1% olivine microphenocrysts (altered) max: 0.5 mm, mod: 0.2 mm.

GROUNDMASS: fine grained

VESICLES: 15%, elongate, subrounded, mainly filled with carbonate and minor zeolite

ALTERATION: moderately altered light gray basaltic clast, olivine completely altered to iddingsite

VEINS:

OCCURRENCE: 1R 1A 16-21 cm; 3R 3A 67-70.5 cm; 4R 1A 0-20.5 cm (massive zones in clast, vesicular bands type 8), 30-34 cm

==========================================================

TYPE: 4

TEXTURE: highly olivine-phyric basalt

COLOR: reddish gray

PHENOCRYSTS: 20% olivine (altered) max: 5mm, mod: 2 mm

GROUNDMASS: fine grained

VESICLES: 3%, moderate sphericity, subrounded, mainly filled with carbonate and minor zeolite

ALTERATION: moderately to highly altered brownish gray basaltic clast, large amounts of olivine altered to iddingsite

VEINS:

OCCURRENCE: 1R 2A 2.5-5.5 cm; 3R 3A 88.5-97 cm; 6R 1A 1-3.5 cm, 49-53.5 cm

==========================================================

TYPE: 5

TEXTURE: aphyric basalt

COLOR: reddish medium gray to brownish gray

PHENOCRYSTS: 0.5% olivine (altered) microphenocrysts; 0.2% pyroxene microphenocrysts

GROUNDMASS: fine grained

VESICLES: 15%, elongate, subrounded, mainly filled with carbonate and minor zeolite

ALTERATION: moderately to highly altered brownish gray basaltic clast, olivine is altered to iddingsite

VEINS:

OCCURRENCE: 1R 2A 9-15 cm; 1R 3A 48-53 cm, 51-65 cm; 3R 3A 118.5-122 cm; 3R 4A 46-50 cm

==========================================================

TYPE: 6

TEXTURE: moderately plagioclase-phyric basalt

COLOR: reddish medium gray

PHENOCRYSTS: 5% plagioclase (fresh), max: 1.2 mm, mod: 1 mm; olivine microphenocrysts

GROUNDMASS: fine grained

VESICLES: 10%, low sphericity, subrounded, mainly filled with carbonate and minor zeolite

ALTERATION: moderately altered gray basaltic clast, orange alteration halos, olivine is completely altered to iddingsite and plagioclase is partly altered to brown clay

VEINS:

OCCURRENCE: 1R 2A 50-55 cm; 3R 3A 11-14 cm; 3R 4A 19-27.5 cm; 5R 1A 127.5-132.5 cm; 6R 1A 7-15 cm, 98.5-105 cm

==========================================================

TYPE: 7

TEXTURE: highly olivine-augite-phyric basalt

COLOR: medium gray

PHENOCRYSTS: 7% olivine (fresh), max: 5 mm, mod: 4 mm; 5% augite, max: 8 mm, mod: 4 mm; 1% plagioclase, max: 3 mm, mod: 1 mm

GROUNDMASS: fine grained

VESICLES: none, 4% in 6R 2A 27-31 cm and 10% in 7R 1A 56-108 cm

ALTERATION:  highly altered brownish gray basaltic clast, with partely altered olivine to iddingsite

VEINS:  veins filled with blocky and fibrous carbonate

OCCURRENCE: 1R 2A 85.5-1R 3A 9 cm; 1R 3A 41-44 cm; 3R 4A 31-34 cm 5R 1A 49.5-63 cm, 122-127.5 cm, 132.5-136.5 cm, 5R 2A 4-8 cm, 16-27 cm, 27.5-47 cm, 102-119.5 cm, 122-125 cm; 125.5-130 cm, 130.5-147 cm; 6R 1A 16-25.5 cm, 60.5-65.5 cm, 72-78 cm, 81-84 cm, 85-96.5 cm; 6R 2A 27-31 cm (highly augite-olivine-phyric basalt; pyroxene 10%, max 1.2 mm, mod 0.6 mm; olivine (completely altered) 5%, max 3, mod 1 mm; 4% vesicles, more vesicular type 7); 7R 1A 56-108 cm (10% vesicles, filled; more vesicular type 7)

==========================================================

TYPE: 8

TEXTURE: aphyric basalt

COLOR: brown orange gray

PHENOCRYSTS: none

GROUNDMASS: fine grained

VESICLES: 10%, elongate, subangular, mainly filled with carbonate and minor zeolite

ALTERATION:

VEINS:

OCCURRENCE: 3R 3A 106.5-112.5 cm; 3R 4A 14.5-18 cm; 4R 1A 0-20.5 cm (vesicular bands in clast, more massive zones type 3)

==========================================================

TYPE: 9

TEXTURE: highly plagioclase-phyric basalt

COLOR: medium gray

PHENOCRYSTS: plagioclase 10%, max 2.5 mm, mod 1.5 mm

GROUNDMASS: fine grained

VESICLES: 1% high, rounded, mainly filled with carbonate and minor zeolite

ALTERATION:

VEINS:

OCCURRENCE: 5R 2A 0-3.5 cm, 48.5-51.5 cm

==========================================================

TYPE: 10

TEXTURE: aphyric

COLOR: pale orange gray

PHENOCRYSTS: none

GROUNDMASS: fine grained

VESICLES: 15%, low, subrounded, max 10 mm, mode 4 mm, mainly filled with carbonate and minor zeolite

ALTERATION:

VEINS:

OCCURRENCE: 6R 1A 26.5-35 cm, 35-37.5 cm, 38.5-43 cm, 44-48 cm

==========================================================

TYPE: 11

TEXTURE: aphyric basalt

COLOR: medium gray

PHENOCRYSTS: plagioclase laths, microphenocrysts (laths)

GROUNDMASS: fine grained

VESICLES: 10%, low to elongate, subrounded

ALTERATION:

VEINS:

OCCURRENCE: 6R 1A 106-114 cm; 6R 2A 26-33 cm

==========================================================

TYPE: 12

TEXTURE: aphyric basalt

COLOR: brownish red

PHENOCRYSTS: none

GROUNDMASS: fine grained

VESICLES: 0.5%, low to elongate, subrounded

ALTERATION:

VEINS:

OCCURRENCE: 6R 2A 31-37 cm

# Comments

Avoid splitting sections between different pages if possible